Block truncation coding

- Divide the image into 4(4 blocks

- Quantize the pixels in the block into two values

Parameter m=16 is the number of pixels in the block, and q is the number of pixels quantized to b-value.

Absolute moment BTC:

Encoding in the BTC

Encode the blocks by:

- Block parameters (,) by (k=8 bits each, 2k=16 bits in total)

- Bit plane describing the segmentation (m=16 bits)

- Constant bit rate of   bits per pixel

- With 4(4 block size this is 2 bpp (4:1 compression)

Numerical example:

Bit-plane of BTC:

Improvements to the BTC

Quadtree segmentation:

- Divide the image into m1 m1 blocks.

- Apply BTC if the standard deviation ( of a block is less than a threshold th

- Otherwise divide into four subblocks and repeat the same process

- Block division is performed until:

  - threshold criterion is met, or

  - the minimal block size (m2 m2) is reached.

- The hierarchy of the blocks is represented by a quadtree structure.

Compressing the quantization parameters:

- The pair (a,b) can be compressed by forming two subsample images; one from the a-values and another from the b-values.

- These can then be compressed by any lossless (or even lossy) image compression algorithm. For example: FELICS.

Compressing the bit plane:

- Lossless binary image compression method (e.g. JBIG)

- Filtering the bit-plane

- Vector quantization

- Sub-sampling and interpolating missing pixels

Original				  1 bit per pixel

bpp=8.00     mse=0		  bpp=2.00     mse=35.54

Interpolation 75 %			     Interpolation 50 %			Interpolation 25 %

bpp=1.75     mse=38.85	     bpp=1.50     mse=41.93	       bpp=1.25     mse=63.83

1D median filtering			     VQ					       Prediction technique

bpp=1.75     mse=46.46	     bpp=1.50     mse=48.29	       bpp=1.50     mse=101.48

Comparison of the BTC variants

Elements of the combined BTC algorithm:

| Part: | Method: |
| --- | --- |
| Quantization | AMBTC |
| Coding of (a,b): | FELICS |
| Coding of bitplane: | VQ / 256 entries |
| Block size: | 3232 22 |

Eye compressed by BTC:

# BTC	AMBTC	HBTC-VQ

bpp =  2.00	bpp =  2.00	bpp =  1.62

mse = 43.76	mse = 40.51	mse = 15.62

SCALAR QUANTIZATION

VECTOR QUANTIZATION

Definition of vector quantization (VQ)

Data:

X		Set of N input vectors X={x1,x2,…,xN}

P		Partition of M clusters P={p1, p2,…,pM}

C		Cluster centroids C={c1, c2,…,cM}

Goal:

Find such C and P to minimize f(C, P)

Error function:

Example of vector quantization

996 data vectors in 2-dimensional vector space

Clustering the vector space into 256 clusters

Use of VQ in image compression

Normalizing the image blocks for VQ

Choice of predictor in mean-removed VQ:

100 normalized sample 4(4 blocks from Eye

Codebook organization

Classified vector quantization

Representation of solution

Partition

Codebook

Main approaches

- Hierarchical methods

- Build the clustering structure stepwise:

- Splitting approach (top-down):

  - Increase clusters by adding new ones

  - For example: divide the largest cluster

- Merge-based approach (bottom-up):

  - Decrease clusters by removing existing ones

  - For example: merge existing clusters

- Iterative methods

- Take any initial solution, e.g. random clustering

- Make small changes to the existing solution by:

  - Descendent method (apply rules that improve)

  - Local search (trial-and-error approach)

Generalized Lloyd algorithm (GLA)

Partition step:

Centroid step:

GLA (X,P,C): returns (P,C) REPEAT FOR i:=1 TO N DO Pi ( FindNearestCentroid(xi,C) FOR i:=1 TO M DO Ci ( CalculateCentroid(X,P,i) UNTIL no improvement.

Splitting approach

Split Put all vectors in one clusters; REPEAT Select cluster to be split; Split the cluster; UNTIL final cluster size reached;

Median cut algorithm

(example)

Median cut + GLA

(example)

PCA-based splitting

1. Calculate the principal axis.

2. Select the dividing point P at the principal axis.

3. Partition according to hyperplane.

4. Calculate two centroids of the two subclusters.

Time complexity of splitting

- Assume clusters of n vectors with K values (K=3 for RGB);

- Principal axis calculated in O(nK2) time

- Selection of dividing point in O(n(logn) time

- Assume that largest cluster is split to equal halves: n ( n/2

- Total number of vectors is:

(

Total time complexity is O(NK2 logM ) + O(N logN )

Splitting experiments

With partition refinement:

Quality-time comparison:

Merge-based approach: PNN algorithm

PNN Put all vectors in own cluster; REPEAT (a,b) (SearchClusterPair; MergeClusters(a,b); UNTIL final cluster size reached;

Iterative shrinking

IS(X, M) ® S FOR i(1 to N DO si ( {xi}; REPEAT sa ( SearchClusterToBeRemoved(S); RepartitionCluster(S, sa); UNTIL ¦S¦=M;

Results using merge-approach (PNN)

Split and merge

Generate an initial codebook by any algorithm. Repeat Select a cluster to be split. Split the selected cluster. Select two clusters to be merged Merge the selected clusters Until no improvement achieved.

Comparison of Split and Merge

Structure of Local Search

Generate initial solution. REPEAT Generate a set of new solutions. Evaluate the new solutions. Select the best solution. UNTIL stopping criterion met.

Neighborhood function using random swap:

Object rejection:

Object attraction:

Randomized local search

| RLS algorithm 1: C ( SelectRandomDataObjects(M). P ( OptimalPartition(C). REPEAT T times Cnew ( RandomSwap(C). Pnew ( LocalRepartition(P,Cnew). Cnew ( OptimalRepresentatives(Pnew). IF f(Pnew, Cnew) < f(P, C) THEN (P, C) ( (Pnew, Cnew) | RLS algorithm 2: C ( SelectRandomDataObjects(M). P ( OptimalPartition(C). REPEAT T times Cnew ( RandomSwap(C). Pnew ( LocalRepartition(P,Cnew). GLA(Pnew,Cnew). IF f(Pnew, Cnew) < f(P, C) THEN (P, C) ( (Pnew, Cnew) |
| --- | --- |

Random swap

BEFORE SWAP

AFTER SWAP

Local fine-tuning

LOCAL REPARTITION

AFTER GLA

Genetic algorithm

Structure of Genetic Algorithm

Genetic algorithm: Generate S initial solutions. REPEAT T times Generate new solutions. Sort the solutions. Store the best solution. END-REPEAT Output the best solution found. Generate new solutions: REPEAT S times Select pair for crossover. Cross the selected solutions. Mutate the new solution. Fine-tune the new solution by GLA. END-REPEAT

Pseudo code for the GA   (1/2)

CrossSolutions(C1, P1, C2, P2) ( (Cnew, Pnew) Cnew ( CombineCentroids(C1, C2) Pnew ( CombinePartitions(P1, P2) Cnew ( UpdateCentroids(Cnew, Pnew) RemoveEmptyClusters(Cnew, Pnew) PerformPNN(Cnew, Pnew) CombineCentroids(C1, C2) ( Cnew Cnew ( C1 ( C2 CombinePartitions(Cnew, P1, P2) ( Pnew FOR i(1 TO N DO IF THEN ELSE END-FOR

Pseudo code for the GA   (2/2)

UpdateCentroids(C1, C2) ( Cnew FOR j(1 TO ¦Cnew¦ DO ( CalculateCentroid(Pnew, j ) PerformPNN(Cnew, Pnew) FOR i(1 TO ¦Cnew¦ DO qi ( FindNearestNeighbor(ci) WHILE ¦Cnew¦>M DO a ( FindMinimumDistance(Q) b ( qa MergeClusters(ca, pa, cb, pb) UpdatePointers(Q) END-WHILE

Combining existing solutions

Performance comparison of GA