JPEG

- JPEG (Joint photographic experts group) is joint result by:

  - International organization for standardization (ISO)

  - International Telegraph and Telephone Consultative Committee (CCITT)

  - International Electrotechnical Committee (IEC)

- The JPEG standard includes the following modes of operation:

  - Lossless coding

  - Sequential coding

  - Progressive coding

  - Hierarchical coding

Compression:

Decompression:

Discrete cosine transform

1-dimensional

DCT transform:

Inverse transform:

Scaling factor:

Discrete cosine transform

2-dimensional

DCT transform:

Inverse transform:

DCT basis functions for N=8:

2-D DCT basis functions for N=4

Examples of DCT for sample 4(4 blocks

| ORIGINAL IMAGE |  | TRANSFORMED IMAGE |
| --- | --- | --- |
| FLAT |
| 10 | 10 | 10 | 10 |  | 40.0 | 0.0 | 0.0 | 0.0 |
| 10 | 10 | 10 | 10 |  | 0.0 | 0.0 | 0.0 | 0.0 |
| 10 | 10 | 10 | 10 |  | 0.0 | 0.0 | 0.0 | 0.0 |
| 10 | 10 | 10 | 10 |  | 0.0 | 0.0 | 0.0 | 0.0 |
| RANDOM TEXTURE |
| 11 | 15 | 18 | 14 |  | 58.8 | 0.3 | -1.8 | 1.3 |
| 14 | 11 | 13 | 12 |  | -3.9 | -2.8 | -3.5 | 2.6 |
| 15 | 16 | 19 | 12 |  | 2.7 | -1.7 | 1.2 | -3.4 |
| 18 | 17 | 12 | 18 |  | 3.0 | -0.9 | -5.3 | 1.8 |
| IMPULSE |
| 10 | 10 | 10 | 10 |  | 42.5 | 1.4 | -2.5 | -3.2 |
| 10 | 20 | 10 | 10 |  | 1.4 | 0.7 | -1.4 | -1.8 |
| 10 | 10 | 10 | 10 |  | -2.5 | -1.4 | 2.5 | 3.3 |
| 10 | 10 | 10 | 10 |  | -3.2 | -1.8 | 3.3 | 4.3 |
| LINE (horizontal) |
| 10 | 10 | 10 | 10 |  | 50.0 | 0.0 | 0.0 | 0.0 |
| 10 | 10 | 10 | 10 |  | -5.4 | 0.0 | 0.0 | 0.0 |
| 20 | 20 | 20 | 20 |  | -10.1 | 0.0 | 0.0 | 0.0 |
| 10 | 10 | 10 | 10 |  | 13.1 | 0.0 | 0.0 | 0.0 |
| EDGE (vertical) |
| 10 | 10 | 20 | 20 |  | 60.0 | -18.4 | 0.0 | 7.7 |
| 10 | 10 | 20 | 20 |  | 0.0 | 0.0 | 0.0 | 0.0 |
| 10 | 10 | 20 | 20 |  | 0.0 | 0.0 | 0.0 | 0.0 |
| 10 | 10 | 20 | 20 |  | 0.0 | 0.0 | 0.0 | 0.0 |
| EDGE (horizontal) |
| 10 | 10 | 10 | 10 |  | 60.0 | 0.0 | 0.0 | 0.0 |
| 10 | 10 | 10 | 10 |  | -18.4 | 0.0 | 0.0 | 0.0 |
| 20 | 20 | 20 | 20 |  | 0.0 | 0.0 | 0.0 | 0.0 |
| 20 | 20 | 20 | 20 |  | 7.7 | 0.0 | 0.0 | 0.0 |
| EDGE (diagonal) |
| 10 | 10 | 10 | 10 |  | 55.0 | -11.1 | 0.0 | -0.7 |
| 10 | 10 | 10 | 20 |  | -11.1 | 5.0 | 4.6 | 0.0 |
| 10 | 10 | 20 | 20 |  | 0.0 | 4.6 | -5.0 | -1.9 |
| 10 | 20 | 20 | 20 |  | -0.7 | 0.0 | -1.9 | 5.0 |
| SLOPE (horizontal) |
| 10 | 12 | 14 | 16 |  | 52.0 | -8.9 | 0.0 | -0.6 |
| 10 | 12 | 14 | 16 |  | 0.0 | 0.0 | 0.0 | 0.0 |
| 10 | 12 | 14 | 16 |  | 0.0 | 0.0 | 0.0 | 0.0 |
| 10 | 12 | 14 | 16 |  | 0.0 | 0.0 | 0.0 | 0.0 |

Quantization in JPEG

Quantization equation:

- ci is the original transform coefficient (real number)

- q is the quantization factor (ingeteger between 1..255)

- The result is rounded to the nearest integer

Example of quantization by factor of 2:

Dequantization:

Possible quantization tables:

| Uniform quantization |  | More accurate quantization |  | Less accurate quantization |
| --- | --- | --- | --- | --- |
| 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  | 1 | 2 | 2 | 4 | 4 | 8 | 16 | 16 |  | 8 | 64 | 64 | 128 | 256 | 256 | 256 | 256 |
| 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  | 2 | 4 | 8 | 8 | 8 | 16 | 16 | 32 |  | 64 | 128 | 128 | 128 | 256 | 256 | 256 | 256 |
| 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  | 4 | 4 | 8 | 16 | 16 | 16 | 32 | 32 |  | 128 | 256 | 256 | 256 | 256 | 256 | 256 | 256 |
| 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  | 4 | 8 | 16 | 16 | 16 | 32 | 32 | 32 |  | 256 | 256 | 256 | 256 | 256 | 256 | 256 | 256 |
| 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  | 8 | 16 | 16 | 32 | 32 | 32 | 32 | 32 |  | 256 | 256 | 256 | 256 | 256 | 256 | 256 | 256 |
| 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  | 8 | 16 | 16 | 32 | 32 | 32 | 64 | 64 |  | 256 | 256 | 256 | 256 | 256 | 256 | 256 | 256 |
| 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  | 16 | 16 | 32 | 32 | 32 | 32 | 64 | 64 |  | 256 | 256 | 256 | 256 | 256 | 256 | 256 | 256 |
| 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  | 16 | 16 | 32 | 32 | 32 | 64 | 64 | 64 |  | 256 | 256 | 256 | 256 | 256 | 256 | 256 | 256 |

Quantization tables in JPEG:

|  | Luminance |  | Chrominance |
| --- | --- | --- | --- |
|  | 16 | 11 | 10 | 16 | 24 | 40 | 51 | 61 |  | 17 | 18 | 24 | 47 | 99 | 99 | 99 | 99 |
|  | 12 | 12 | 14 | 19 | 26 | 58 | 60 | 55 |  | 18 | 21 | 26 | 66 | 99 | 99 | 99 | 99 |
|  | 14 | 13 | 16 | 24 | 40 | 57 | 69 | 56 |  | 24 | 26 | 56 | 99 | 99 | 99 | 99 | 99 |
|  | 14 | 17 | 22 | 29 | 51 | 87 | 80 | 62 |  | 47 | 66 | 99 | 99 | 99 | 99 | 99 | 99 |
|  | 18 | 22 | 37 | 56 | 68 | 109 | 103 | 77 |  | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 |
|  | 24 | 35 | 55 | 64 | 81 | 104 | 113 | 92 |  | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 |
|  | 49 | 64 | 78 | 87 | 103 | 121 | 120 | 101 |  | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 |
|  | 72 | 92 | 95 | 98 | 112 | 100 | 103 | 99 |  | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 |

Entropy coding:

- Huffman or arithmetic coding.

- The first coefficient (denoted by DC-coefficient) is separately coded from the rest of the coefficients (AC-coefficients).

- The DC-coefficient is by predicting from the DC-coefficient of the previous block.

- The prediction error is coded using as in lossless JPEG

- The AC-coefficients are coded one in the order given by zig-zag scanning

- Simple run-length coding is applied:

  - All sub-sequent zero-value coefficients are coded by the run-length

  - Huffman coding is then applied to the non-zero coefficients.

JPEG for color images:

RGB color images are compressed in JPEG by transforming the image first into YUV (or YIQ in the case of North America) and then compressing the three color components separately. The chrominance components are often sub-sampled so that 22 block of the original pixels forms a new pixel in the sub-sampled image. The color component images are then upsampled to their original resolution in the decompression phase.

Progressive mode:

Progressive JPEG is rather trivial. Instead of coding the image block after block, the coding is divided into several stages. At the first stages the DC-coefficients are coded from each block. The decoder can get rather good approximation of the image on the basis on the DC-coefficients alone, since they contain the information of the average value of the blocks. At the second stage, the first significant AC-coefficients (determined by the zig-zag order) are coded. At the third phase the next significant AC-coefficients are coded, and so on. In total, there are 64 coefficients in each block, so the progressive coding can have at most 64 stages. In practice, the progressive coding can be changed back to the sequential order for example already after the first stage. This is because the DC-coefficients are usually enough for the decoder to decide whether the image is worth retrieving.

Hierarchical mode:

- A reduced resolution version of the image is compressed

- followed by the higher resolution versions in increasing order.

- In each case the resolution is doubled

Example of a block compressed by JPEG:

|  | Original block |  | Transformed block |
| --- | --- | --- | --- |
|  | 139 | 144 | 149 | 153 | 155 | 155 | 155 | 155 |  | 235.6 | -1.0 | -12.1 | -5.2 | 2.1 | -1.7 | -2.7 | 1.3 |
|  | 144 | 151 | 153 | 156 | 159 | 156 | 156 | 156 |  | -22.6 | -17.5 | -6.2 | -3.2 | -2.9 | -0.1 | 0.4 | -1.2 |
|  | 150 | 155 | 160 | 163 | 158 | 156 | 156 | 156 |  | -10.9 | -9.3 | -1.6 | 1.5 | 0.2 | -0.9 | -0.6 | -0.1 |
|  | 159 | 161 | 162 | 160 | 160 | 159 | 159 | 159 |  | -7.1 | -1.9 | 0.2 | 1.5 | 0.9 | -0.1 | 0.0 | 0.3 |
|  | 159 | 160 | 161 | 162 | 162 | 155 | 155 | 155 |  | -0.6 | -0.8 | 1.5 | 1.6 | -0.1 | -0.7 | 0.6 | 1.3 |
|  | 161 | 161 | 161 | 161 | 160 | 157 | 157 | 157 |  | 1.8 | -0.2 | 1.6 | -0.3 | -0.8 | 1.5 | 1.0 | -1.0 |
|  | 162 | 162 | 161 | 163 | 162 | 157 | 157 | 157 |  | -1.3 | -0.4 | -0.3 | -1.5 | -0.5 | 1.7 | 1.1 | -0.8 |
|  | 162 | 162 | 161 | 161 | 163 | 158 | 158 | 158 |  | -2.6 | 1.6 | -3.8 | -1.8 | 1.9 | 1.2 | -0.6 | -0.4 |
|  | Quantization matrix |  | Quantized coefficients |
|  | 16 | 11 | 10 | 16 | 24 | 40 | 51 | 61 |  | 15 | 0 | -1 | 0 | 0 | 0 | 0 | 0 |
|  | 12 | 12 | 14 | 19 | 26 | 58 | 60 | 55 |  | -2 | -1 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | 14 | 13 | 16 | 24 | 40 | 57 | 69 | 56 |  | -1 | -1 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | 14 | 17 | 22 | 29 | 51 | 87 | 80 | 62 |  | -1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | 18 | 22 | 37 | 56 | 68 | 109 | 103 | 77 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | 24 | 35 | 55 | 64 | 81 | 104 | 113 | 92 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | 49 | 64 | 78 | 87 | 103 | 121 | 120 | 101 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | 72 | 92 | 95 | 98 | 112 | 100 | 103 | 99 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | Dequantized coefficients |  | Decompressed block |
|  | 240 | 0 | -10 | 0 | 0 | 0 | 0 | 0 |  | 144 | 146 | 149 | 152 | 154 | 156 | 156 | 156 |
|  | -24 | -12 | 0 | 0 | 0 | 0 | 0 | 0 |  | 148 | 150 | 152 | 154 | 156 | 156 | 156 | 156 |
|  | -14 | -13 | 0 | 0 | 0 | 0 | 0 | 0 |  | 155 | 156 | 157 | 158 | 158 | 157 | 156 | 156 |
|  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  | 160 | 161 | 161 | 162 | 161 | 159 | 157 | 155 |
|  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  | 163 | 163 | 164 | 163 | 162 | 160 | 158 | 156 |
|  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  | 163 | 164 | 164 | 164 | 162 | 160 | 158 | 157 |
|  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  | 160 | 161 | 162 | 162 | 162 | 161 | 159 | 158 |
|  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  | 158 | 159 | 161 | 161 | 162 | 161 | 159 | 158 |

Original									JPEG

bpp = 8.00 			mse = 0.00			bpp = 1.00 			mse = 17.26

JPEG									JPEG

bpp = 0.50 			mse = 33.08			bpp = 0.25 			mse = 79.11

Figure 4.26: Magnifications of Lena compressed by JPEG.